## Slide 1
Architecture for An Indoor Distributed Cyber-Physical System Composed of Mobile Robots and Fog Computing Nodes
Objective
Develop an architecture for providing localization information to robots using StarL across the view of multiple Kinect cameras connected to x86 MinnowBoards in a Fog Computing fashion
References
[1] J. M. O’Kane, A Gentle Introduction to ROS. Independently published, Oct. 2013, available at http://www.cse.sc.edu/∼jokane/agitr/.
[2] N. Hervey, “Localization and Control of Distributed Mobile Robots with the Microsoft Kinect and StarL”, April 2016
Approach
StarL and examples are available at: https://github.com/verivital/starl
2 types of ROS nodes: Central Command, and Robot Observer
Central Command records position information and informs each Robot Observer node which drones to look for
Robot Observer nodes process the Kinect image and report location information to the Central Command node
Remaining and Future Work
Finish writing code
Fix issues between Kinect and MinnowBoard
Validate system design
Add more drone types to the system
Motivation
The current system uses a single Kinect camera which limits the total field of view. By adding more Kinect cameras, the area covered by the localization method is expanded so tests can be run across a larger area. Additionally, the architecture could be used for other, similar distributed systems
Nathaniel Paul Hamilton ● PhD Student at Vanderbilt University, Electrical Engineering ● nathaniel.p.hamilton@vanderbilt.edu ● Advisor: Dr. Taylor Johnson
Acknowledgments
I am not sure what to put here
Current Setup [1]
Desired Setup
Central Command Code Schematic
Robot Observer Code Schematic
Central Command Subscription List
/kinect#/locations
  List of robot names and location information
/kinect#/response
  Report from indicating whether or not a robot was found crossing its boundaries
Robot Observer Subscription List
/botID_list
  Full list of robot names, types, and colors
/shutdown
/kinect#/bot_list
  A list of robots to track
/kinect#/incoming
  A list of robots to watch the boundaries for
Localization Example